## Slide 1: IT694 Computer Networks Week10_Lec1
Routing algorithms

## Slide 2: Routing algorithm classification
global or decentralized information?
global: all routers have complete topology, link cost info
“link state” algorithms
decentralized: iterative process of computation, exchange of info with neighbors
routers initially only know link costs to attached neighbors
“distance vector” algorithms
How fast do routes change?
dynamic: routes change more quickly
  periodic updates or in response to link cost changes
static: routes change slowly over time

## Slide 3: Distance vector algorithm
Based on Bellman-Ford (BF) equation (dynamic programming):
Let Dx(y): cost of least-cost path from x to y.
Then:
Dx(y) = minv { cx,v + Dv(y) }
Bellman-Ford equation
min taken over all neighbors v of x
v’s estimated least-cost-path cost to y
direct cost of link from x to v

## Slide 4: Bellman-Ford Example
u
y
z
2
2
1
3
1
1
2
5
3
5
Suppose that u’s neighboring nodes, x,v,w, know that for destination z:
Du(z) = min { cu,v + Dv(z),
cu,x + Dx(z),
cu,w + Dw(z) }
Bellman-Ford equation says:
Dv(z) = 5
v
Dw(z) = 3
w
Dx(z) = 3
x
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum (x) is next hop on estimated least-cost path to destination (z)

## Slide 5: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)
Dx(y) ← minv{cx,v + Dv(y)} for each node y ∊ N
when x receives new DV estimate from any neighbor, it updates its own DV using B-F equation:

## Slide 6: Distance vector algorithm:
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
wait for (change in local link cost or msg from neighbor)
each node:
distributed, self-stopping: each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors – only if necessary
  no notification received, no actions taken!
recompute DV estimates using DV received from neighbor
if DV to any destination has changed, notify neighbors

## Slide 7: Distance vector: example
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=0
All nodes have distance estimates to nearest neighbors (only)
A few asymmetries:
missing link
larger cost
d
e
f
a
b
c
All nodes send their local distance vector to their neighbors

## Slide 8: Distance vector example: iteration
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c

## Slide 9: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1
compute
compute
compute
compute
compute
compute
compute
compute
compute

## Slide 10: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1

## Slide 11: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2

## Slide 12: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
8
1
2
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2
compute
compute
compute
compute
compute
compute
compute
compute
compute

## Slide 13: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2

## Slide 14: Distance vector example: computation
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
b receives DVs from a, c, e
a
b
c
d
e
f
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞

## Slide 15: Distance vector example: computation
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=1
b receives DVs from a, c, e, computes:
a
b
c
d
e
f
DV in b:
Db(f) =2
Db(g) = ∞
Db(h) = 2
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = 2
  Db(e) = 1
e
compute
b
Db(a) = min{cb,a+Da(a), cb,c +Dc(a), cb,e+De(a)} = min{8,∞,∞} = 8
Db(c) = min{cb,a+Da(c), cb,c +Dc(c), c b,e +De(c)} = min{∞,1,∞} = 1
Db(d) = min{cb,a+Da(d), cb,c +Dc(d), c b,e +De(d)} = min{9,2,∞} = 2
Db(f) = min{cb,a+Da(f), cb,c +Dc(f), c b,e +De(f)} = min{∞,∞,2} = 2
Db(i) = min{cb,a+Da(i), cb,c +Dc(i), c b,e+De(i)} = min{∞, ∞, ∞} = ∞
Db(h) = min{cb,a+Da(h), cb,c +Dc(h), c b,e+De(h)} = min{∞, ∞, 2} = 2
Db(e) = min{cb,a+Da(e), cb,c +Dc(e), c b,e +De(e)} = min{∞,∞,1} = 1
Db(g) = min{cb,a+Da(g), cb,c +Dc(g), c b,e+De(g)} = min{∞, ∞, ∞} = ∞

## Slide 16: Distance vector example: computation
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
c receives DVs from b
a
b
c
d
e
f
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞

## Slide 17: Distance vector example: computation
g
h
i
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
c receives DVs from b computes:
a
b
c
d
e
f
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
Dc(a) = min{cc,b+Db(a}} = 1 + 8 = 9
Dc(b) = min{cc,b+Db(b)} = 1 + 0 = 1
Dc(d) = min{cc,b+Db(d)} = 1+ ∞ = ∞
Dc(e) = min{cc,b+Db(e)} = 1 + 1 = 2
Dc(f) = min{cc,b+Db(f)} = 1+ ∞ = ∞
Dc(g) = min{cc,b+Db(g)} = 1+ ∞ = ∞
Dc(i) = min{cc,b+Db(i)} = 1+ ∞ = ∞
Dc(h) = min{cbc,b+Db(h)} = 1+ ∞ = ∞
DV in c:
  Dc(a) = 9
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = 2
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
compute
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 18: Distance vector example: computation
1
1
1
1
1
1
1
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
e receives DVs from b, d, f, h
a
b
c
DV in f:
  Dc(a) = ∞
  Dc(b) = ∞
  Dc(c) = ∞
  Dc(d) = ∞
  Dc(e) = 1
  Dc(f) = 0
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = 1
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞
DV in h:
  Dc(a) = ∞
  Dc(b) = ∞
  Dc(c) = ∞
  Dc(d) = ∞
  Dc(e) = 1
  Dc(f) = ∞
  Dc(g) = 1
  Dc(h) = 0
Dc(i) = 1
DV in d:
  Dc(a) = 1
  Dc(b) = ∞
  Dc(c) = ∞
  Dc(d) = 0
  Dc(e) = 1
  Dc(f) = ∞ Dc(g) = 1
  Dc(h) = ∞
Dc(i) = ∞
d
e
f
g
h
i
Q: what is new DV computed in e at t=1?
compute

## Slide 19: Distance vector: state information diffusion
t=0
c’s state at t=0 is at c only
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
c’s state at t=0 has propagated to b, and may influence distance vector computations up to 1 hop away, i.e., at b
t=1
c’s state at t=0 may now influence distance vector computations up to 2 hops away, i.e., at b and now at a, e as well
t=2
c’s state at t=0 may influence distance vector computations up to 3 hops away, i.e., at d, f, h
t=3
c’s state at t=0 may influence distance vector computations up to 4 hops away, i.e., at g, i
t=4
Iterative communication, computation steps diffuses information through network:
t=1
t=2
t=3
t=4

## Slide 20: Distance vector: link cost changes
“good news
travels fast”
t0 : y detects link-cost change, updates its DV, informs its neighbors.
t1 : z receives update from y, updates its DV, computes new least cost to x , sends its neighbors its DV.
t2 : y receives z’s update, updates its DV. y’s least costs do not change, so y does not send a message to z.
link cost changes:
node detects local link cost change
updates routing info, recalculates local DV
if DV changes, notify neighbors
x
z
1
4
50
y
1

## Slide 21: Distance vector: link cost changes
link cost changes:
node detects local link cost change
“bad news travels slow” – count-to-infinity problem:
x
z
1
4
50
y
60
y sees direct link to x has new cost 60, but z has said it has a path at cost of 5. So y computes “my new cost to x will be 6, via z); notifies z of new cost of 6 to x.
z learns that path to x via y has new cost 6, so z computes “my new cost to x will be 7 via y), notifies y of new cost of 7 to x.
y learns that path to x via z has new cost 7, so y computes “my new cost to x will be 8 via y), notifies z of new cost of 8 to x.
z learns that path to x via y has new cost 8, so z computes “my new cost to x will be 9 via y), notifies y of new cost of 9 to x.
…
see text for solutions. Distributed algorithms are tricky!