## Slide 1: IT694 Computer Networks
Week10_Lec2
Routing Information Protocol

## Slide 2
Distance Vector Routing
Each node collects the knowledge of the entire network, and shares it periodically (e.g.
every 30 seconds) only with its neighbors. The knowledge is a sequence of messages:
{<source node> <dest. node> <next node> <total cost>}
Each message shows "so far optimal" route from the <source node> to the
<destination node>, where the first leg of the optimal route is <next node>, and
the total minimal cost is <total cost>.
The cost is expressed in terms of number of hops.
By getting such messages, the nodes can combine them in order to build their routing
Table - eliminate duplicates by cost minimization
This is a distributed implimentation of the Bellman-Ford algorithm for finding the shortest path through a network.
This table is being updated continuously and shared with the node's neighbors.

## Slide 3
rnetwork the whole
E I periodically send to my knowledge about
the whole internetwork to A.
Distance
Vector
Routing
I periodically send
about
my knowledge
about
I periodically send my knowledge about the whole internetwork to C, E.
I periodically send my knowledge about the whole internetwork to A, D.
I periodically send my knowledge
the whole network to B, F,
.
I periodically send my
knowledge about the
whole internetwork
to A, C.
network to B, D.

## Slide 4: Initial Routing tables

## Slide 5
DV Routing
(cont.)
Tables
13-12
Final
Routing

## Slide 6: Routing Information Protocol
A simple intra-domain protocol
Straightforward implementation of Distance Vector Routing
Each router advertises its distance vector every 30 seconds (or whenever its routing table changes) to all of its neighbors
RIP always uses 1 as link metric

## Slide 7: Routing with RIP
Initialization: Send a request packet (command = 1, address family=0..0) on all interfaces:
  RIPv1 uses broadcast if possible,
  RIPv2 uses multicast address 224.0.0.9, if possible
  requesting routing tables from neighboring routers
Request received: Routers that receive above request send their entire routing table
Response received: Update the routing table
Regular routing updates: Every 30 seconds, send all or part of the routing
tables to every neighbor in an response message
Triggered Updates: Whenever the metric for a route change, send the entire routing table.

## Slide 8
13-25
Routing Information Protocol
The simplest and the most widely used routing protocol in IP networks. Uses UDP for transport over the well-known port 520.
RIP
Message
Format
Address
1 – request
2 - response
family
identifier (TCP/IP
= 2)
Destination network (uses network rather router address)
Hop count between the advertising
router and the destination network
(value from 1 to 15; 16 means “network
unreachable”
than
An element of distance vector
The “next-hop” field is missing here.
It is included in the new version of RIP, RIP-2.

## Slide 9: RIP Updating Algorithm
Case a
Case b

## Slide 10
DV Routing (cont.)
13-9
Updating
RT (Cont.)
4
Case a
Router
X
Network
N
1
Router
A
If optimal route AN goes via X it
means that X is closer to N than A and therefore has to be trusted more, so the entry AN via X = 2 is replaced by
AN via X = 5
RT of A
Updated
RT of A
replace
Advertising message from
X
increment
X  N cost = 4
X N cost = 5
AN via X cost = 5
. . . . . . . . . . . . . . . . .
N via X cost = 2
. . . . . . . . . . . . . . . . .

## Slide 11
DV Routing (cont.)
Updating RT
13-10
4
Case b
Router
X
Network
N
1
2
Router
A
This time the advertising router (X) is not
equal to next hop (Y), therefore the entry will be:
1
min{AN
via Y = 3, N via X = 5}
Router
Y
RT
of A
Updated
RT of A
minimize
Advertising message from X
increment
X N cost = 4
X N cost = 5
AN via Y cost = 3
. . . . . . . . . . . . . . . . .
AN via Y cost = 3
. . . . . . . . . . . . . . . . .

## Slide 12
DV Routing (cont.)
13-11
Example
of
updating
a
routing
table
New
RT
of
router X
Old
RT of router X
If the entry “Net2 5” is to be accepted by the router X, then the next hope for that entry would be C.
NOTICE: This example is not related to example networks on previous slides.

## Slide 13
13-27
What is the periodic response sent by router R1 in figure below?
Assume
R1
knows about the whole autonomous
system.
R1 can advertise three networks 144.2.7.0, 144.2.9.0, and
144.2.12.0.
The periodic response (update packet) is shown in next slide.
Example 1

## Slide 14
13-28
Periodic packet sent from
router
R1 to
its neighbors:

## Slide 15
13-29
RIP
timers
which is reset whenever an update
180 seconds, the corresponding entry
distance to infinite (16).
Timer per route (entry).
arrives. If the update doesn’t arrive in
is marked invalid by setting the
Timer per route (entry).
All invalid entries are purged 120 seconds after being determined invalid by X-timers. This gives a
chance that other routers learn that the specified network is unreachable
from this router.
Timer per router. Controls the advertising (time is a random number between 25-35 sec to avoid synchronization)

## Slide 16
13-31
Drawbacks of RIP:
Slow convergence
Too simple
Instability
Scalability
metric

## Slide 17
13-32
Slow convergence
Periodic advertisement every 30 seconds,
average propagation
time is
30/2
= 15
seconds
n x 15 s
This router learns about the change in
network 1 after n x 15 seconds.
(if n = 20, the delay would be 5 minutes)
Suppose there is a
change in network 1
In order to limit the delay, max hop count is limited to 15.
All entries that have distance 16 are considered invalid and are purged. Consequently the diameter of an AS that uses RIP is limited to15 hops.

## Slide 18
Instability
13-33
Loops of routing packets.
Limiting the hops to 15 helps but doesn’t solve the problem.
Net 1 fails. A updates its RT
with cost = 16, but advertises this after delay (max 30 sec).
In the meantime B sends
update with cost = 2. A chooses the cost 2+1 = 3, which is smaller than 16.
This continues until finally
realizes that the Net 1 is unreachable.
B

## Slide 19
13-34
Remedies to Instability
Triggered updates
Split
horizons
Split
horizons
with
Poisoned
reverse

## Slide 20
13-35
Triggered Updates
If there is a change in the router sends the update immediately
instead of waiting the update time (30 sec). Each router that receives information about change, forwards the update immediately.
This helps
in case from the previous slide,
but doesn’t help in case
of
a
router
failure
(because
there
is
no
one
to
report
such
change).

## Slide 21
13-36
Split horizon
Router never advertises the cost of a destination to neighbor N
if N is the current next-hop for the destination
If a router has received an update from an interface, then this same
update
information
must not be forwarded
back
to the
same
interface.
B has received info about Net 1 and Net
through the right i/f only.
2 through its left i/f. This
info is forwarded
Router A is closer to destination (Net 1) than the router B, therefore there is not
meaningful that B supplies A with information about something that is closer to A.

## Slide 22
13-37
Split Horizon with Poisoned Reverse
Same
idea,
but
instead
of
no
advertisement
use
infinity
cost
The erroneous route will be eliminated within the interval of 180 seconds.